## Slide 1: Unit, Integration, and System Testing Examples for Automotive Applications

## Slide 2: Unit Testing Example: Obstacle Detection Algorithm
Component: Obstacle Detection Module
Description: Validate that the obstacle detection algorithm correctly identifies obstacles within a specified range.
Input:
- Sensor data: [{distance: 1.5m, objectType: 'vehicle'}, {distance: 0.8m, objectType: 'pedestrian'}]
- Threshold distance: 1.0m
Expected Output:
- Obstacles within threshold: [pedestrian]
Pass Criteria: The module returns only obstacles within the specified threshold.
Tool: Google Test (C++), JUnit (Java).

## Slide 3: Integration Testing Example: Obstacle Detection and Emergency Braking
Modules: Obstacle Detection Module and Emergency Braking Module
Description: Verify that the emergency braking module receives accurate obstacle data and triggers braking when necessary.
Input:
- Obstacle detected at 0.8m by the obstacle detection module.
- Vehicle speed: 60 km/h.
Expected Output:
- Emergency braking system is activated.
- Braking signal is sent to the brake actuator.
Pass Criteria: Emergency braking is triggered within the required response time (< 200ms).
Tool: Postman (API testing), CANoe (for automotive network communication).

## Slide 4: System Testing Example: Obstacle Avoidance Maneuver
System: Advanced Driver Assistance System (ADAS)
Description: Validate the system's ability to detect an obstacle and steer the vehicle to avoid it.
Scenario:
- Vehicle speed: 80 km/h.
- Obstacle detected at 30m.
- Road type: Two-lane highway.
Expected Output:
- Vehicle steers to the adjacent lane to avoid the obstacle without crossing the speed limit.
- No collision occurs.
Pass Criteria: The vehicle avoids the obstacle safely and continues in the correct lane.
Tool: Driving simulator (e.g., PreScan, dSPACE), HIL (Hardware-in-the-Loop).

## Slide 5: Summary of Test Levels
Unit Testing:
- Tests individual functions or components in isolation.
Integration Testing:
- Validates interactions between components or modules.
System Testing:
- Tests the complete system in end-to-end scenarios.
Each level is essential to ensure the reliability, safety, and performance of automotive systems.